## Slide 1
Beyond MIMO:
Media-based Wireless
Canada Research Chairs
Aug. 10th 2012
Amir K. Khandani
B.Sc./M.Sc. Tehran University, Ph.D. McGill University
Canada Research Chair
RIM-NSERC Industrial Research Chair
E&CE Department, University of Waterloo
khandani@uwaterloo.ca, 519-8851211 ext 35324

## Slide 2: A New Paradigm in Wireless: Media-based vs. (legacy) Source-based
Main idea:
  Embed the information in the variation of the RF channel external to the antenna.
Benefits vs. (legacy) source-based wireless:
    Additive information over multiple receive antennas (similar to MIMO) with the advantages of:
      Using a single transmit antenna
      Independence of noise over receive antennas
    Inherent diversity over a static channel (constellation diversity) using single or multiple antenna(s)
      Diversity order improves with the number of constellation points
      Unlike MIMO, diversity does not necessitates sacrificing the rate
      It essentially coverts the Raleigh fading channel into an AWGN channel with the same average receive energy and with a minor loss in capacity.
    Harvesting transmit energy using multiple receive antennas

## Slide 3
Keep the source shining and change the media
Enjoy rich variations with small changes in media
Rich scattering environment: slightest perturbation in the environment causes independent outcomes.
Variations of phase is critical and can be exploited with stable TX/RX synchronization using two-way link (continually sending back pilot from RX to TX).
Media-based Wireless
Data
Carrier
Exponential growth due to rich scattering

## Slide 4: How to Change the RF Channel? Just An Example
Separately control some of RF properties, i.e. of each surface, e.g., on-off partial mirrors, according to the input data (media-based) or randomly (security).
More details at: www.cst.uwaterloo.ca/2way
Surfaces with
controllable
RF properties
Enhancing rich scattering (near field reflections & openings in walls for wave to exit)
Antenna sending a
Fixed/shaped carrier

## Slide 5: Media-based: Signaling Scheme
T
T
LT
Total signal energy: LE
Basis: Orthogonal
Complex Dimensions: L
T
Raleigh channel of impulse response of length L.
E
Media-based
one complex
dimension
Coded Data
At these times, coded (FEC) bits are used to select one of possible channel states.

## Slide 6: Media-based: Rate
6
Carrier
(unit energy)
Vectors of Dimension K
K = # of Receive Antennas
m: Data
: K-D constellation (iid Gaussian elements)
For low SNR, i.e., prior to
saturation to

## Slide 7: Media-based vs. Source-based
E
Data
Parallel
SISO
K complex
dimensions
Media-based
one complex
dimension
Total signal energy: E
Basis: non-orthogonal
Complex Dimensions/sec/Hz: K
Better Performance
KxK
MIMO
K complex
Dimensions
E/K
E/K
E/K
H
E/K
E/K
E/K
Total signal energy: LKE
Basis: Orthogonal
Complex Dimension/sec/Hz: K
Total signal energy: E
Basis: Orthogonal
Complex Dimensions/sec/Hz: K

## Slide 8: Media-based vs. Legacy Systems: Effective Dimensionality
: Eigenvalues of a KxK Wishart random matrix
1xK Media-based
KxK legacy MIMO
Legacy SISO
Rate=log(1+E)
E
Rate

## Slide 9: Asymptotic Gain (for E∞) in Rate and Energy

## Slide 10: Asymptotic Gain (for E∞) in Energy & Rate
K | L | KL |  | 
1 | 2 | 2 | 4.2 bits | 6.4 dB
2 | 1 | 2 | 4.2 bits | 9.4 dB
1 | 4 | 4 | 13.0 bits | 9.8 dB
4 | 1 | 4 | 13.0 bits | 15.8 dB
1 | 8 | 8 | 34.8 bits | 13.1 dB
8 | 1 | 8 | 34.8 bits | 22.1 dB
1 | 16 | 16 | 86.4 bits | 16.2 dB
16 | 1 | 16 | 86.4 bits | 28.2 dB

## Slide 11: Media-based vs. Legacy Systems: Slope of Rate vs. SNR (dB) at SNR=0
Legacy SISO: Slope=1
Legacy KxK MIMO: Maximum eigenvalue of a KxK Wishart matrix (upper limited by 4)
1xK Media-based: LK
 | L=1, K=2 | L=1, K=4 | L=1, K=8 | L=1, K=infinity
KxK MIMO | 1.75 | 2.45 | 2.96 | 4
1xK Media-based | 2 | 4 | 8 | Infinity

## Slide 12: Media-based vs. Legacy MIMO
MIMO works well only at high SNR values, but in some applications, e.g., optical transmission where MIMO is formed over different polarizations, or very lower power wireless, it is important to use spatial degrees of freedom offered by multiple antennas to save energy.
2 or 4 antenna with a rate of 4 bits/s/Hz/antenna is typical in current systems
L=1,K=2
L=1,K=4
Relative Gain of Media-based will be much higher for L>1, typically L>>1

## Slide 13: Media-based vs. Legacy MIMO
1xK media-based is significantly simpler than KxK MIMO.
At low SNR, unlike MIMO, media-based is optimum.
At high SNR, energy saving of media-based vs. MIMO is significant and increases with the number of antennas.
8 antenna systems with a rate of 4 bits/s/Hz/antenna
L=1,K=8
Relative Gain of Media-based will be much higher for L>1, usually L>>1.

## Slide 14: Some Remarks
Power spectrum for media-based:
  Linear time-varying (LTV) while legacy systems are linear time-invariant (LTI).
  LTV can cause frequency expansion.
  Received Power Spectrum: Average of channels’ spectrums times input spectrum
  Input spectrum is shaped to limit the bandwidth.
Equalization:
  Channels with an impulse response of length L provides L extra dimensions per receive antenna (inserting time gaps between subsequent transmissions).

## Slide 15: Gain due to Inherent Diversity: Typicality of Random Constellation
m: Data
AWGN:
Carrier of Energy E

## Slide 16
Modeling Discrete Constellation= Additional Additive Noise Variance of Additional Noise Power
Two dimensional space:

## Slide 17: Example for Behavior of Mean and Standard Deviation of Additional Noise
 | 2 dimensions (Q=1) | 4 dimensions (Q=2) | 8 dimensions (Q=4)
Mean | 0.0078 | 0.1619 | 0.9140
Standard Deviation | 0.0078 | 0.0870 | 0.1363
Constellation with L=256 points

## Slide 18: Inherent Diversity Gains
TX energy for RX SNR of 20dB with P(outage)=0.1 is 50dB, Gain=30dB
TX energy for RX SNR of 20dB with P(outage)=0.01 is 60dB, Gain=40dB
TX energy for RX SNR of 20dB with P(outage)=0.01 is 70dB, Gain=50dB
Mutual Information of 1000 randomly generated two dimensional constellations (generated with Gaussian PDF).
256 QAM

## Slide 19: SISO Case Revisited
TX block is a train of K consecutive base TX signals, followed by L-1 zeros prior to the next TX block.
Channel in changed in each of K time slots among 2r possibilities, resulting in a linear system with a random impulse response.
  Time shift in input results in the same time shift in the response.
  Oversample RX signal (sum of time-shifted responses) by L.
    KL samples are full rank, yielding LK2/(L+K-1) dimensions per unit time.
    Extra dimensions are correlated, degrading the performance.
    Noise is correlated, improving the performance.
    Iterative or Trellis decoding can be used for detection.
  Source code-book is composed of a discrete set of shells (circular shells) with uniform phase.

## Slide 20: More discussion on Media-based, including discussions on embedding information in both source and channel are at: www.cst.uwaterloo.ca

## Slide 21: Realizing (external to antenna) RF Perturbation
Objective: Create several random, selectable, options for propagation path
  Simpler than traditional beam-forming
    No need for tuning/control, having specific patterns, or concentration of energy

## Slide 22: Candidates for RF Channel Perturbation
Photonic microwave
  Changing waveguide property by surface plasma generated through light source
    Uses several photo masks for plasma grating
  Creating surface plasma in an external to antenna parasitic object
    Uses light intensity to change plasma depth
Electrically tunable impendence surface
  Leaky wave antenna (based on a waveguide with tunable surface leakage)
  Electrically changeable impedance surface as an external to antenna parasitic element
Changing the permeability of ferrite under the effect of a magnetic field (e.g., via a current-carrying coil)
Changing the permittivity of ferroelectric material under the effect of an electric field (e.g., via a bias voltage)
Using meta-material as an external to antenna parasitic object with changeable refraction index

## Slide 23: Security Applications: One-time Pad (Vernam Cipher)

## Slide 24: Unbreakable Security: Vernam Cipher, One-time Pad
Vernam Cipher, One-time Pad: Bit-wise XOR of a (non-reusable) mask with the message
Generalization:
  Happens naturally in wireless transmission
    Each random phase can completely mask one PSK symbol.
+
Z
Y=X+Z (mod 2), X,Y,Z are binary, I(X;Y)=0
X
Z
Y=X+Z (mod 2π), X,Y,Z are angle, I(X;Y)=0
X
+

## Slide 25: Exploiting Channel Randomness to Share a Common Phase (Key)
Closed loop gain is unique to Alice and Bob (determined by the fine details of the propagation path between them).
After extracting , RF environment around Alice and/or Bob is perturbed and a new phase value is extracted.

## Slide 26: Key Generation: A Simpler Approach
I1
G12
G21
Eve
?
?
TX
RX
MOD
DEM
Baseband
Baseband
RX
MOD
TX
DEM
I2
G22
G11
O1
O2

## Slide 27: Exploiting Channel Randomness to Share a Common Phase (Key)
Key Point: Each TX antenna should be used only once for each channel perturbation.
Challenges:
  Synchronizing the two parties to agree on phase.
  Providing a new common random phase for each PSK symbol.
  Two-way wireless solves both these challenges.
  Errors in common phase values are corrected by the overall channel code.
  Hardware implementation shows that the common phase values can be measured with very high precision.

## Slide 28: Exploiting Channel Randomness to Share a Common Phase (Key)
Two algorithms are provided for key generation.
  Please see www.cst.uwaterloo.ca/2way for details.

## Slide 29: More discussion on security, including discussions on causing confusion using legitimate jamming, embedding information in both source and channel are at: www.cst.uwaterloo.ca

## Slide 30: Thank You! Questions/Comments?
Amir K. Khandani
E&CE Department, University of Waterloo
khandani@uwaterloo.ca, 519-8851211 ext 35324